Solenoids

- At what distance away from a wire carrying 5.0 A is the magnetic field strength 8.00 x 10-5 T?

- What is the magnetic field strength 25.0 cm away from a long straight wire carrying a current of 1.80 A?

- Which of the following best describes the magnetic field inside a current-carrying solenoid as you move from A to B.

- The current through a solenoid is varied and the resulting magnetic field at its centre is recorded in each case. A graph of the magnetic field versus the current is produced. Which of the following represents the slope of this graph?

- A solenoid has a length of 0.30 m, a diameter of 0.040 m and 500 windings. The magnetic field at its centre is 0.045 T. What is the current in the windings?

- The magnetic field at the centre of a solenoid of length 0.25 m is 1.2 102 T. The current in the windings is 7.5 A. How many windings does the solenoid have?

- Protons travelling at 2.2 ×105 m/s enter at right angles to a magnetic field. The field is produced by a 0.16 m long solenoid. A current of 5.3 A flows through the 820 turns of wire of the solenoid.

- What is the magnetic field in the solenoid?

- What is the radius of curvature of the proton beam in the magnetic field of the solenoid?

- An electron travelling at 7.7 ×106 m/s enters at right angles into a uniform magnetic field. Inside the field the path of the electron has a radius of 3.5 ×10-2 m.

- What is the magnitude of the magnetic field?

- If the magnetic field is produced at the centre of a solenoid by a current of 0.62 A, what is the number of turns per unit length of the solenoid?

- A 0.20 m long solenoid has 750 turns of copper wire and the magnetic field near its centre is measured to be 3.0 ×10 T. What is the current flowing through the solenoid?

A. 1.6 A

B. 6.4 A

C. 32 A

D. 160 A

- What is the magnetic field strength 25.0 cm away from a long straight wire carrying a current of 1.80 A? 1.44 x 10-6 T

- A solenoid with 2500 turns and length of 15 cm has a current of 4.8 A passing through it. What is the magnetic field strength at the centre of the solenoid?

- A solenoid produces a magnetic field strength of 1.0 x 10-3 T in its centre when 4.0 A flows through its 20.0 cm length. How many turns does the solenoid have?

- A thin, 20.0 cm long solenoid has a total of 600 turns of wire and carries a current of 1.50 A. Calculate the field inside the solenoid, near the center.

- A proton travelling at 2200 m s enters a 0.15 T magnetic field perpendicularly.

- What is the magnitude of the proton’s acceleration while travelling through the magnetic field?

- What is the radius of the proton’s circular path while travelling through the magnetic field?

- A section of conductor is carrying a current due south, as shown below. Due to the presence of a magnetic field, the conductor experiences a magnetic force to the right. What is the direction of the magnetic field?

A. left

B. right

C. into the page

D. out of the page

Answers:

- 0.0125 m

- 1.44x 10-6 T

- A

- A

- 21 A

- 320

- 3.41x10-2 T, 6.73x10-2 m

- 1.3x10-3 T, 1600/m

- B

- 1.44 x 10-6 T

- 0.100 T

- 40 turns

- 0.00565 T

- 3.16x1010 m/s2, 1.5x10-4 m

- C